# USB DISK preparation

Requirements:

- Microsoft Windows Vista

- Insert a blank USB disk in the system: wait until Windows detect the removable disk and install the correct drivers

- run "diskpart" system tool (from cmd.exe)

- on prompt, type "list disk"

- check the usb removable disk number (usually disk 1)

- type "select disk <number_of_the_usb_disk>"

- type "clean”

- type “create partition primary”

- type "select partition 1"

- type "active"

- type “format fs=fat32”

- type “assign”

- type "exit"