## Slide 1: Project X
Mass interception of encrypted connections

## Slide 2: What?
SSL/TLS interception
TOR interception

## Slide 3
...a thorny path

## Slide 4: Common Issues
Public Key Pinning avoids rogue CA to sign certs

## Slide 5: Common Issues
Google and Facebook actively search for rogue CA signed certs
(no more governmental signing: France, India)

## Slide 6: Common Issues
HSTS enforces https on a variety of hardcoded website (no more SSL-strip)

## Slide 7: Common Issues
HTTPS Everywhere enforces https and could send rogue certificates to the EFF SSL Observatory

## Slide 8: Common Issues
No solution for sniffing TOR available by now on the market

## Slide 9
The Solution

## Slide 10: How?
Place an in-line Active Probe in the ISP’s network

## Slide 11: How?
Exploit the target transparently by injecting a browser-based exploit while he’s surfing the web (http)

## Slide 12: How?
Insert a trusted root CA certificate(s) for MITM
Redirect first TOR hop

## Slide 13: How?
Decrypt and Decode the traffic!

## Slide 14
More in depth

## Slide 15: Deployment phases
Identification
Inoculation/Marking
SSL MITM (only for SSL)
Decoding
Maintenance

## Slide 16: Identification Phase
Uniquely identify a target on the internet
(cookies, browser strings, etc.)
Create a profile for each target to know if it’s exploitable
Avoid exploiting the same target “too much”
Avoid exploiting a target with “problematic” AV

## Slide 17: Inoculation Phase
HTTP man-in-the-middle (transparent proxy)
Browser based exploits (all platforms)
Local to root exploits (sandbox escape)
Methods to insert root CA cert(s) into the keystore
Methods to divert TOR first HOP

## Slide 18: Marking Phase
Insert a “watermark” in target’s environment to uniquely identify “inoculated” targets during SSL connections
Setting different TOR’s SOCKS password

## Slide 19: SSL MITM Phase
Transparent proxy performing
SSL MITM only on “marked” targets
Serve the right certificate
Avoid exposing fake certs
Avoid checks to detect fake certs

## Slide 20: Decoding Phase
A good partner with a consolidated decoding technology

## Slide 21: Maintenance Phase
Automatic test to check if the certs are invalidated
(Customer side)

## Slide 22: Maintenance Phase
Automatic check for exploits effectiveness
Automatic check for inoculation phase
(HT side)

## Slide 23
Challenges

## Slide 24: Identification Phase
Targets using multiple browsers
Targets behind routers (NAT)
Targets behind a TCP Proxy
Targets changing IP address often

## Slide 25: Inoculation Phase
Build or Buy exploits for several platforms
Write shellcodes to insert root CA certs
Write shellcodes to modify TOR environment

## Slide 26: Marking Phase
Marking the target cipher suites list
Using client-side certificate
(both good but fragile)

## Slide 27: Marking Phase
IP-to-Target Mapping
Less reliable
Same problems as Identification

## Slide 28: Marking Phase
Mixed approach is possible
fake https image request
host file modification
Marking must survive browser/os upgrades!

## Slide 29: SSL MITM Phase
Find an appliance to handle the inline traffic
(no single point of failure)

## Slide 30: SSL MITM Phase
Pay attention to Extended Validation certificate
Pay attention to EFF SSL Observatory
Pay attention to Trust Assertion for Cert Keys (TACK)

## Slide 31: Decoding Phase
Where do we send sniffed traffic??

## Slide 32: Feasibility Matrix
 | Windows |  | OSX | Linux | iOS | Android
Exploit | IE | FF | Safari | Firefox | Safari | Browser
 | Chrome |  | Chrome | Chrome | Chrome | Chrome
Root |  |  |  | Not needed (per user) |  | 
Cert |  |  |  |  |  | 
Finger (hello) | IE | FF | Safari | Firefox | Safari | Browser
 | Chrome |  | Chrome | Chrome | Chrome* | Chrome
Finger (client cert) | IE | FF | Safari | Firefox | Safari | Browser
 | Chrome |  | Chrome | Chrome | Chrome** | Chrome
** Does not support client certs
* Does not trust local CA certs

## Slide 33: Weak Points
Heavily relies on browser remote-to-root exploit availability
TOR manipulation is possible only through clear-text traffic
Browser/OS vendors may change parameters we use for identification

## Slide 34: Weak Points
Certificate revocation leads to target loss
(impact reduced by using several certificates)
AV may detect our shellcodes
(…btw no target loss)
Mass deployment increases the risk of leaking

## Slide 35
And finally…

## Slide 36: Strengths
Our solution bypasses certificate pinning since it uses a custom CA “manually” installed!!!
Our solution bypasses HSTS

## Slide 37: Strengths
Our solution bypasses active MITM detection (France should have known it)
Our solution is the only way to intercept TOR traffic at the moment

## Slide 38
Decisions

## Slide 39: Hardware for the probes
iBypass TAP
General purpose server
Modifying an existing SSL appliance

## Slide 40: Decoding the traffic
Once decrypted the traffic must be decoded:
Forwarding to an existing monitoring center using standard protocols
Create a turn-key solution with a “passive” partner

## Slide 41
Resources

## Slide 42: Time
First Minimal Demo: 2 months
First POC: 9 months
First Deployment: 15 months

## Slide 43: Human
2 Exploit/Shellcode Developers
1 Network/Probe Developer
1 ISP SysAdmin (consultancy)
2 Backend/Logic Developers
1 Tester
In house but allocated

## Slide 44
Future development

## Slide 45: Other over-SSL protocols
Support for imaps, pops, etc.

## Slide 46: RCS integration
Keep a DB of exploitable targets
Exploit them again to install RCS
Integration through the RCS Console
(…or HT Monitoring Center)

## Slide 47: Layer 3 MITM
Just mangle the handshake and forward the rest of the connection to improve performances

## Slide 48: SSL TLS key dump
Just save the SSL keys and pass it to an SSL offload decrypter for maximum performances

## Slide 49
Technical details

## Slide 50: General Architecture
Command & Control
Probe
Probe
Probe
Anon Net

## Slide 51: Command & Control
Ruby on Rails
HTML5 interface
Fault tolerant & scalable

## Slide 52: Command & Control
Exploit repository (auto update from HT)
Attack rules (global or per probe)
Active/identified targets in realtime
Probes configuration / update
Anon network configuration
Global system monitoring

## Slide 53: Anon Network
Used to forward connections to public addresses to the probes
Useful if we set a socks/proxy in the target and the target is nomadic

## Slide 54: Probe Architecture
Bypass TAP
Probe
Bridge
Target Identifier & Hijacker
HTTP
HTTPS
SSL MITM Proxy
TOR Proxy
Exploiter
Forwarder
ADMIN