IP and networking basics
1 febbraio 2011

---
Summary
- OSI stack & TCP/IP architecture
- IP Addressing
- Lab

---
OSI stack & TCP/IP architecture
- OSI - layered model concept
    - Divide-and-conquer approach
    - Dividing requirements into groups
    - Each group can be referred to as a layer
      - Upper layers are logically closer to the user and deal with more abstract data, relying on lower layer protocols to translate data into forms that can eventually be physically transmitted
    - Open Systems Interconnection Reference Model (OSI-RM) adopted as a standard for networking

---
- What is TCP/IP?
    - In simple terms, it is a language that enables communication between computers
    - A set of rules (protocol) that define how two computers address each other and send data to each other
    - It is a suite of protocols named after the two most important protocols TCP and IP but includes other protocols such as UDP, ICMP, RTP, etc

---
- Application
    - Upper layers
    - Application oriented
    - Indipendent of layers below
- Transport
    - Lower layers
    - Transmission of data

---
TCP/IP layer model

---
OSI and TCP/IP model comparison

---
- Layer 1: Physical layer
    - Moves bits using voltage, light, radio, etc.
    - No concept of bytes or frames
    - Bits are defined by voltage levels, or similar physical properties

---
- Layer 2: Data link layer
    - Provides reliable transit of data across a physical network link
    - Bundles bits into frames and moves frames between hosts on the same link
    - A frame has a definite start, end, size
    - Often also a definite source and destination link-layer address (i.e. Ethernet MAC address)

---
- Layer 3: Network layer
    - Routes the information in the network
    - i.e. IP is a network layer implementation which defines addresses in such a way that route selection can be determined
      - Adds an additional layer of addressing, i.e. IP address, which is different from MAC address
      - It allows packets to travel from one LAN to another one

---
- Layer 3: Network layer (i.e. IP)
    - Unreliable
      - If packet gets lost, network layer doesn’t care
      - Higher layers can resend lost packets
    - Forwards packets hop by hop
      - Encapsulates network layer packet inside data link layer 2 frames
      - Receive from one link, forward to another link
      - There can be many hops from source to destination

---
- Layer 3: Network layer (i.e. IP)
    - Makes routing decisions
      - How can the packet be sent closer to its destination?
      - Forwarding and routing tables embody “knowledge” of network topology
      - Routers can talk to each other to exchange information about network topology

---
- Layer 3: Network layer (i.e. IP)
    - Routers make routing decisions
      - OSPF and BGP are the main dynamic routing protocols. All routes have a weigth and the lightest path is chosen according to each destination
      - Injecting fake “light” routes could cause packets to follow a different route than normal and allows intercepting traffic (i.e. China did it a few years ago...by mistake? :) )

---
- Layer 4: Transport layer
    - Provides end to end transportation of segments
    - i.e. TCP
      - adds reliability by detecting and retransmitting lost packets
      - uses acknowledgements and sequence numbers to keep track of successful, out-of-order and lost packets
    - UDP is much simpler but... no reliability features!

---
Traceroute
- Interactive session:
  See packets flow with traceroute and tcptraceroute
  (Traceroute uses UDP, tcptraceroute uses TCP)
- Traceroute www.cisco.com
- Tcptraceroute www.cisco.com 80
  (why akamaitechnologies.com??)

---
- Layer 5: Session layer
    - Organizes and synchronizes the exchange of data between application processes
- Layer 6: Presentation layer
    - Converts data from applications into common format and vice versa

---
- Layer 7: Application layer
    - Provides different services to the applications
    - Uses the underlying layers to carry out work i.e. SMTP (mail), HTTP (web), Telnet, FTP, DNS
    - Exploits usually target this layer

---
- Questions
    - What is the difference between network layer and transport layer?
    - Which layer the HTTP protocol belongs to?

---
Lower layers add headers (and sometimes trailers) to data from higher layers

---
- Layer 2: Ethernet frame
    - Destination and source are 48-bit MAC addresses

---
- Layer 3: IP datagram
    - Source and Destination are 32-bit IP addresses
    - “Dotted quad”, i.e. 127.0.0.1

---
- Layer 4: TCP segment
    - Source and Destination are 16-bit TCP port numbers (IP addresses are implied by the IP header)
    - IANA “well known” port numbers, ie.
      SSH = 22
      Telnet = 23
      FTP =21
      SMTP = 25
      Etc. etc.

---
- Questions
    - Is a data packet bigger at transport layer or at network layer?
    - Why the IP address is not enough to correctly identify a service connected to a network?

---
IP addressing
- Purpose of an IP address
    - Identifies a machine’s connection to a network
    - Physically moving a machine from one network to another might require changing the IP address (Why “might” instead of “must?”)
    - TCP/IP uses unique 32-bit addresses

---
IP addressing
- Basic structure of an IP address
    - 32 bit number (4 octet number): i.e. 133.27.162.125
    - Decimal representation
    - Binary representation
133	27	162	125
10000101	00011011	10100010	01111101

---
IP addressing
- IP address allocation
    - Private IP address ranges:
      - 10/8 (10.0.0.0 – 10.255.255.255)
      - 192.168/16 (192.168.0.0 – 192.168.255.255)
      - 172.16/12 (172.16.0.0 – 172.31.255.255)
    - Loopback addresses:
      127.0.0.0/8
    - Public IP address space
      - Assigned by an appropriate authority such as RIPE, ARIN, AFRINIC, etc. or Local Internet Registries (LIRs)

---
IP addressing
- IP address ownership
    - Whois services answer the question “Who owns this IP address?”

---
IP addressing
- Network masks
    - Network Masks help define which bits are used to describe the Network Part and which bits describe hosts
    - Different Representations
      - Decimal dot notation: 255.255.224.0
      - Binary: 11111111 11111111 11100000 00000000
      - Number of network bits: /19
    - Binary AND of 32 bit IP address with 32 bit netmask yields network part of address

---
IP addressing
- Questions
    - Which of these are valid public IP addresses?
      - 192.168.1.1
      - 217.56.23.211
      - 256.15.31.7
    - How many IP addresses does a /24 subnet contain?
    - What is the IP address 127.0.0.2? Is it valid? What for?

---
Network Address Translation
- A way to “add” more IP addresses
- One to one
- One to many
- Many to many
- Many to one

---
Lab
- See how IPs, ports and MAC address change when a packet travels from a host to another host
- Traffic sniffing
    - Wireshark/tshark
    - Ngrep – network grep
- Arp poisoning
    - Cain & Abel
    - Ettercap